## Slide 1: Drought Planning Through Integrated Rate Design
Drew Atwater
Water Resources Manager
Moulton Niguel Water District
October 8, 2015

## Slide 2: Agenda
District background
Historical demand management actions
Components of integrated rates
Rate design
Drought Actions
Results
What’s next?

## Slide 3: About MNWD
Water, recycled water & sewer service
  170,000 people
  5 Cities in South Orange County
100% dependent on imported water
  MWD (≈ 29,000 AFY)
Recycle Water ≈ 25% Total Demand
Annual budget: $126 M
Key revenues:
  Rates
  Property tax

## Slide 4: Service Area Snapshot
Residential
Median Household Income ~$150,000

## Slide 5: Water Supply
Delta
Colorado River Aqueduct
State Water Project
Sierra Mountains
Moulton Niguel Water District

## Slide 6: Demand Management Efforts
Water Budget Rates Implemented
2015 = Lowest potable water use since 1990
25% Recycled Water

## Slide 7: Rate History
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Historic | 0.18947 | 0.083333 | 0.28487 | 0.16246 | 0.16119 | 0.16327 | 0.07
Approved | 0.07 | 0.05
Projected | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04
7 annual rate increases in the past 30 years
Water Budget Based Rates implemented in 2011
  2009 Drought enforcement experience
  Need for demand management tool
7
Adopted new rates Feb. 11, 2015

## Slide 8: Components of Integrated Rates
Drought planning
Behavioral change
Prop. 218
Marketing
Capital intensive industry
Local agency outreach
Internal coordination

## Slide 9: What is a Water Budget?
Allocation of usage based on characteristics that impact demand
Example:
  Indoor Allocation
    Household Size
    Efficient Indoor Use (45 to 75 GPCD)
  Outdoor Allocation
    ET (Seasonal, Historical Monthly, Actual Districtwide, Actual by microzone)
    Irrigable Area
    Crop Coefficient & Irrigation Efficiency
Notes: Staff review – several internal workshops along with additional subgroup meetings
Review started with why we even started?
Including rate setting model, allocation calculations, variance procedures, rebate program, outreach efforts
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 10: Indoor Allocation Methods
Household Size
  Default = Census
  Variances
Determine Efficient Indoor Usage
  Average ~ 60 GPCD
  SBx7-7 = 55 GPCD
Notes: Staff review – several internal workshops along with additional subgroup meetings
Review started with why we even started?
Including rate setting model, allocation calculations, variance procedures, rebate program, outreach efforts
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 11: Ex: Indoor Water Budget
Single Family Residence Attached Home – Condo Apartment
Single Family Residence Attached Home – Condo Apartment
45 - 75 Gallons Per Person Per Day
Notes: Staff review – several internal workshops along with additional subgroup meetings
Review started with why we even started?
Including rate setting model, allocation calculations, variance procedures, rebate program, outreach efforts
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 12: Landscape Allocation Methods
12
Based on landscape area
Plant water needs
Adjusted for climate (evapotranspiration – ET)
Notes: Staff review – several internal workshops along with additional subgroup meetings
Review started with why we even started?
Including rate setting model, allocation calculations, variance procedures, rebate program, outreach efforts
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 13: EX: Single Family Detached Home
Single Family Residence:
Outdoor Allocation:
Irrigated area -GIS mapping
Seasonal needs - ET
Warm season turf
71% irrigation efficiency
Variances Available:
Pool
Additional occupants
Medical needs
Others (livestock, etc.)
+
+
4 people
Notes: Joone

## Slide 14: Water Budget VS. IBR
Inclining Block Rate = Average Allocations
  Efficient Solution but Ignores Distributional Effects
  Ex: Large lots need more water- under-allocation
  Ex: Small lots need less- over-allocation
Water Budget = Individual Allocations
  Sends market signal to use at efficient level
Notes: Staff review – several internal workshops along with additional subgroup meetings
Review started with why we even started?
Including rate setting model, allocation calculations, variance procedures, rebate program, outreach efforts
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 15: Rate Design Considerations
Which Tier(s) have demand response?
Supply MC?
Where is usage relatively constant?
To use fixed cost in low tiers or not?
Careful with allocating fixed costs in high tiers
  Water Budget incentivizes conservation
  Demand reduction w/ fixed costs in high tiers creates financial strain

## Slide 16
Why worry about volatility?

## Slide 17: Planning for Volatility
Lower Tier 1 from 65 to 60 GPCD
Tier 2 with Rate Stabilization Reserve
Tier 3, 4, & 5 set at price of water
49%
8%
7%
11%
0.5%
= Average Annual Revenue 2011 to 2014 by Tier
= Standard Deviation of Annual Revenue 2011 to 2014
Notes: Assessment Approach – How did staff approach the rate structure assessment?
Review the Rate Structure – What is it? How does it work? How are allocations calculated?
History of the Implementation – Assessment and Review of why the system was implemented; overview of the timeline
Program Evaluation – Where and how has the program been effective; What challenges have been identified

## Slide 18: Rate Design
Increased water demand creates increased conservation funding
Decreases in Tier 1 & 2 water use increase net revenue
Increases planned for with Reserves
Units Water Usage
Tier 1
Tier 2
Tier 3
Tier 4
$1.41
$1.61
$2.49
$4.25
Water Budget
Revenue Offset
Revenue Offset
Supply Cost
Escalated Conservation
Supply Cost
Supply Cost
Basic Conservation
Aggressive Conservation
$9.04
Tier 5
Price per ccf
Price of Water

## Slide 19: Drought Penalty Design
Rate design offsets need for drought rates
Penalties to encourage conservation
No penalties for past conservation efforts
$9.04
Units Water Usage
Price per Unit
Tier 1
Tier 2
Tier 3
Tier 4
$1.41
$1.61
$2.49
$4.25
Water Budget
Supply Cost
Supply Cost
Supply Cost
Drought Penalty
Tier 5

## Slide 20: Integrated Drought Actions
Alternate plan approval by SWRCB
  1 of 2 in California
Water Budget Based Rates
Water Shortage Contingency Plan
Customer communications
Recycled Water Master Plan
Partnership with cities
Media
Tier 1
Tier 5
Tier 4
Tier 3
Tier 2
Water Shortage Contingency Plan Stage 2
20%
Penalty

## Slide 21: Customer Communications
Bill Messages
Summer Newsletter
Postcards
Press Release
Newspaper Ads

## Slide 22: Outdoor Focus
50 to 70% for outdoor usage
Approximately 300 million square feet of irrigable area in service area
Approximately 3 million square feet of turf removed
# of Turf Applications

## Slide 23: Results
Exceeded targets for June, July, August, and September
Highest ever percentage of customers within their water budget
Financially stable after greater than 20% reduction in demand
Lowest overall water use since 1990
Currently at approximately 50% of per capita water use in 1991
SWRCB
  Rate Structure - Best Practices/Examples for Conservation Water Pricing
CA Department of Water Resources
  Urban Water Management Plan Case Study
June: 22%
July: 27%
May: 29%
August: 22%
Sept: 26%

## Slide 24: What’s Next?
Research with academic
Institutions to inform innovation
  Stanford- Marketing
  UC Riverside- Rates & Rebates

## Slide 25: The next frontier
  California water data collaborative: putting the entire lifecycle of California's water usage data in a centralized cloud database on a voluntary, bottom up basis.